## Slide 1: [LGC] Understanding the importance of model-free approach + an example implementation
eCAL
Raja Selvakumar
08/13/18

## Slide 2: Dynamic programming: overview
Summary
Minimize cost/maximize benefit using discretized time steps
Sequentially finding optimal solutions to subproblems of the larger problem: value/policy iteration
Creates large state and decision spaces subject to the curses of dimensionality
Bellman principle of optimality: For all k=0,1,…,N-1:
Common applications
Task scheduling, trajectory planning, stochastic control problems
Background
Example
Next Steps
Notes: We find optimal solutions to the subproblems using a value or policy iteration in order to find an optimal solution to the larger problem. DP is subject to the curses of dimensionality: mainly the size of the state, action, and outcome space causing significant increases in complexity.
Notation: ck is the cost function while Vk is the value function. Xk is the state vector while uk is the input vector.

## Slide 3: The actor-critic algorithm: model-based RL
Summary
Adding a “critic” to assess the reward (value) associated with each action (policy)
Approximate dynamic programming (ADP) is a form of this real-time optimal decision-making: critic is the function approximator
Key Equation(s)
Background
Example
Next Steps

## Slide 4: Overall comparison of different RL techniques
 | Simulation | DP | ADP | RL
Temporal dependence | Forward time-stepping | Backward time-stepping | Infinite time horizon; requires state transition information | Infinite time horizon
Required input(s) | Parameters, model dynamics | Parameters, discretized state + control space, model dynamics, reward function | Parameters, initial weights, reward function, control objective | Parameters, control objective
Calculated output(s) | State and output profiles | Output profiles | Output profiles and function approximations | Output profiles
Predicted solution time1 | 1 | - | - | ?
Predicted accuracy | 1 | 0.99 | 0.92 | ?
1Normalized to simulation time, predictions based on preliminary tests/literature estimates
Background
Example
Next Steps
Notes: Please see References slide for selected literature on the topic

## Slide 5: Actor-critic: Algorithm Block Diagram
Critic
Neural Network 1
xk
From DFN
Actor
Neural Network 2
Maximize reward
Need r(xk,uk)
w c,k+1
Grad desc
update critic weights
xk
From DFN
uk
uk
Minimize error
ec = Vk’-(Vk-1’-rk)
To experiments
Vk’
uk*
DFN
EXP
w a,k+1
Grad desc
update actor weights
Vk’
Notes: k denotes each individual time step
ADP assess how good the function approximation is close to the desired reward
We provide the state space and initial control from DFN/other echem model results. Find optimal control to use in experimental controller

## Slide 6: Actor-critic: Critic Overview
Critic
Neural Network 1
xk
From DFN
Jk^
w c,k+1
From reward update
uk
Steps
0. Iterate forward in time
Obtain state information from DFN, construct xk at every time step k
Get control values from Actor, append to xk to construct {x1..m,u1..n}k
Use neural network to predict Jk^
Repeat 1-3 with wc,k+1 calculated from gradient descent algorithm from Reward subroutine
From Actor
To reward
Notes: k denotes each individual time step
ADP assess how good the function approximation is close to the desired reward
We provide the state space and initial control from DFN/other echem model results. Find optimal control to use in experimental controller

## Slide 7: Actor-critic: Critic Visual Representation
x1
xm
.
.
.
.
.
.
u1
un

## Slide 8: ADP: Reward subroutine overview
Maximize reward
From Critic
w c,k+1
From previous fn approximation
r(xk,uk)
Steps
0. Iterate forward in time
Obtain Jk^ from critic
Combine with reward and previous fn approximation to create ec
Minimize 0.5 ec2 over all weights wc
Yield wc, send to Critic
Reward function
To Critic
Jk^
Jk-1^
Notes: k denotes each individual time step
ADP assess how good the function approximation is close to the desired reward
We provide the state space and initial control from DFN/other echem model results. Find optimal control to use in experimental controller

## Slide 9: Actor-critic: Actor overview
Actor
Neural Network 1
xk
From state space
uk
w a,k+1
From reward update
Jk^
Steps
Obtain state information from DFN, construct xk at every time step k
Initialize weights: wa(1) and wa(2)
Use neural network to predict Jk^
Repeat 1-3 with wc,k+1 calculated from gradient descent algorithm from Reward subroutine
From Critic
To reward
Notes: k denotes each individual time step
ADP assess how good the function approximation is close to the desired reward
We provide the state space and initial control from DFN/other echem model results. Find optimal control to use in experimental controller

## Slide 10: References
[1] Wahl et. al, 2014. IEEE ISVP. doi: 10.1109/IVS.2014.6856459
[2] Nascimento et. al, 2007. IEEE ISADPRL. doi: 10.1109/ADPRL.2007.368169
[3] Scott et. al, Operations Research. Accessed online.
[4] Dong et. al, 2011. ICAR. Accessed online.
[5] Zhang et. al, 2017. IEEE TSG. doi: 10.1109/TSG.2015.2505298
[6] van der Herten et. al, 2016. arXiv preprint arXiv:1608.04550
[7] Li et. al, 2018. IEEE TITS. Advance Online Publication.
[8] Xu et. al, 2018. AiMES. Submitted abstract online.

## Slide 11: Backup

## Slide 12: Dynamic programming: algorithm
Step 1: Load parameters and discretized state space
Step 2: Iterate backwards in discretized time
Step 3: Create ‘for’ loops for each state
Step 4: Set bounds on control space based on min/max formulation
e.g.
Step 5: Solve Bellman equation at each time point
e.g.
Step 6: Repeat
Step 7: Simulate over control matrix given initial state values
Background
Example
Next Steps

## Slide 13: Approximate dynamic programming: sample algorithm
Step 1: Load parameters and initial weights/other ADP parameters
Step 2: Iterate forward in discretized time
Step 3: Create ‘for’ loop for function approximation subroutine
Step 4: Initialize Actor/Critic to obtain a) J^ and b) u*
Step 5: Compute state transition given prior model dynamic information
Step 6: Repeat
Advantage: Reduce time required to compute value function at each time step
Disadvantage: Reduction in model accuracy and still requiring knowledge of system
Background
Example
Next Steps

## Slide 14: Model based RL: Actor overview- parameter list
Expression | Size | Coming from? | Going to?
xk: State vector | [m,1] | Input neurons | σa
wa(1): 1st weighting matrix | [Nah,m] | Input neurons | σa
σa: Σwai,k(1)xik | [Nah,1] | Input neurons | qa
qa: Φ(σa) -> tanh(0.5σa) | [Nah,1] | σa | Hidden neurons
wa(2): 2nd weighting matrix | [n,Nah] | Hidden neurons | μa
μa: Σwaz,k(2)qaz | [n,1] | Hidden neurons | un
un: Φ(μa) -> tanh(0.5μa) | [n,1] | μa | Output neurons
Jk^: Function approximation |  |  | 
Notes: k denotes each individual time step
ADP assess how good the function approximation is close to the desired reward
We provide the state space and initial control from DFN/other echem model results. Find optimal control to use in experimental controller

## Slide 15: Model-free reinforcement learning: overview
Summary
Model-free framework to obtain optimal control decisions
Actor interacts with environment, adapts based on stimulus reaction
Tradeoff of removing model dynamics vs accuracy in final solution
Useful when analytical methods become infeasible, e.g. finite Markov Decision Problems (MDP), multi-armed bandit problem
Examples
Q-learning, temporal difference
Source: IBM
Background
Example
Next Steps
Notes: Model-free framework is used where an actor obtains a reward from external stimulus with the environment. It subsequently adapts the decision-making process to maximize/minimize the reward.