## Slide 1: RS: Week of 07/23 Update
Raja Selvakumar
7/26/18
eCAL

## Slide 2: Agenda Overview
MATLAB: OCVR/OCVRRC results + discussion
Python: OCVR/OCVRRC update
DP writeup update
ADP OCVR formulation

## Slide 3: OCV-R: MATLAB
DP time: 4.5-6.5 sec
Remarks
Changing objective function has no impact on optimal control
Specifications
ztarget = 0.75
lb:
ub:
State(s): {z}
Control(s): {I}
Objective fn:

## Slide 4: OCV-R-RC: MATLAB
DP time: 10 sec
Specifications
lb:
ub:
State(s): {z, V1}
Remarks
Profile appears to be CV aside from some constraint that becomes active around 248s in a 300s simulation window
Current approaches 0 and SOC approaches target
Notes: Main issue: what happens at 248s?

## Slide 5: Python + writeup status report
[Python]
Code compiles and runs, but results aren’t correct
  Comparing the DP outputs from MATLAB to Python show consistency
  Simulation results show optimal current is just at 0. Interpolation is incorrect
DP takes 5 minutes to run
  Start to parallelize the code (Ray)?
[Writeup]
Complete, addresses recent HEP comments
Notes: Main issue: finding appropriate limits to iterate over for V1

## Slide 6: ADP Sample Algorithm: OCV-R
[Step 1: Actor update to obtain u*]
Step forward in time to obtain optimal control policy at each time step k
  Note all literature shows infinite time horizons, but we can use a finite time horizon [1]
[Step 2: Critic network to obtain J^]
One step approach to calculate J^ using NN
α = 0.9, r = min SOC error obj fun
Notes: [1] https://ris.utwente.nl/ws/portalfiles/portal/5134989/wp_495.pdf

## Slide 7: ADP Algorithm Block Diagram
Critic
Neural Network 1
xk
From DFN
Jk^
Actor
Neural Network 2
Maximize reward
Need r(xk,uk)
w c,k+1
Grad desc
update critic weights
xk
From DFN
uk
uk
Minimize Jk^
To experiments
Jk^
uk*
DFN
EXP
w a,k+1
Grad desc
update actor weights
Notes: k denotes each individual time step
ADP assess how good the function approximation is close to the desired reward

## Slide 8: ADP/RL/DP Workflow Comparison
DP
ADP
RL
Step 1: Construct state and control space (x,u)
Step 2: Policy search (u*)
Iterate backwards in time
Construct entire state and control space
Bellman’s Principle: recurvisely determine optimal control strategy for given value function
Notes: [1] https://ris.utwente.nl/ws/portalfiles/portal/5134989/wp_495.pdf